## Slide 1: Pentesting project walkthrough
LEEDS CITY COLLEGE

## Slide 2
You have been asked by your line manager to test a newly designed and potentially vulnerable webserver. In order to do this safely and without exposing the company network to threat, you have been asked to create a local network and DHCP server as a test lab for this task.
After establishing the network and assigning IP addresses accordingly, you should test for vulnerabilities using a professional suite of tools to access the webserver, obtain admin privileges and identify three crucial pieces of information.
Scenario

## Slide 3: 01
Setting up Kali on VirtualBox

## Slide 8: 02
Setting up Mr Robot on VirtualBox

## Slide 10: 03
Setting up our DHCP server

## Slide 11
vboxmanage (Tool to manage our VMs)
dhcpserver add (Create a DHCP server.)
--network=“name” (We give our network a name.)
--server-ip=10.38.1.1 (Grant an IP address to our server.)
-- lower-ip=10.38.1.110 --upper-ip=10.38.1.120 (Range of IPs to allocate to connected devices is between 110-120.)
--netmask=255.255.255.0 (Assign a network mask to our server.)
-- enable (Initiate server.)

## Slide 12
A DHCP server is a network server that automatically provides and assigns IP addresses, default gateways and other network parameters to client devices. It relies on the standard protocol known as dynamic host configuration protocol or DHCP to respond to broadcast queries by clients.
A DHCP server automatically sends the required network parameters for clients to properly communicate on the network. Without it, the network administrator has to manually set up every client that joins the network, which can be cumbersome, especially in large networks. DHCP servers usually assign each client with a unique dynamic IP address, which changes when the client’s lease for that IP address has expired. By default, your home router will serve as a DHCP server.
The internet protocol (IP) is a protocol, or set of rules, for routing and addressing packets of data so that they can travel across networks and arrive at the correct destination. Data traversing the internet is divided into smaller pieces, called packets. IP information is attached to each packet, and this information helps routers to send packets to the right place. Every device or domain that connects to the internet is assigned an IP address. As packets are directed to the IP address attached to them, data arrives where it is needed.
Once the packets arrive at their destination, they are handled differently depending on which transport protocol is used in combination with IP. The most common transport protocols are TCP and UDP.
DHCP server and IP

## Slide 13
The IP address is a 32-bit number that uniquely identifies a network interface on a machine. An IP address is typically written in decimal digits, formatted as four eight-bit fields separated by full stops. Each eight-bit field represents a byte of the IP address. This form of representing the bytes of an IP address is often referred to as the dotted-decimal format.
The bytes of the IP address are further classified into two parts: the network part and the host part.
10000001.10010000. 00110010.00111000
Network part
This part specifies the unique number assigned to your network. It also identifies the class of network assigned. In the example above, the network part takes up two bytes of the IP address.
Host part
This is the part of the IP address that you assign to each host. It uniquely identifies each machine on your network. Note that for each host on your network, the network part of the address will be the same, but the host part must be different
The IP address

## Slide 14
In TCP/IP, the parts of the IP address that are used as the network and host addresses aren't fixed.
Unless you have more information, the network and host addresses above can't be determined. This information is supplied in another 32-bit number called a subnet mask.
The subnet mask is 255.255.255.0 in this example. It isn't obvious what this number means unless you know 255 in binary notation equals 11111111. So the subnet mask is 11111111.11111111.11111111.00000000.
A netmask is a 32-bit "mask" used to divide an IP address into subnets and to specify the network's available hosts. In a netmask, two bits are always automatically assigned. For example, in 255.255.225.0, "0" is the assigned network address. In 255.255.255.255, "255" is the assigned broadcast address. The 0 and 255 are always assigned and cannot be used.
Netmask

## Slide 15
If we make a mistake or get an error message, we can run the command above to remove the server and start over. Just replace “testlab” with whatever you called your network.

## Slide 16: 04
Firing up our devices on the network we have made

## Slide 17
START KaliLinux on VirtualBox.
Follow through install instructions, clicking “Yes” whenever we are asked if we want to continue with install.
Make sure we install GRUB (this will allow us to boot and load our OS in future).
Keep default settings when asked (unless you want to test things out – it’s OK to break things on a VM).
If we are asked for a server IP, enter the one you made while setting up the DHCP server (in this case 10.38.1.1).
We can set our hostname, domain name, username and password.
START Mr. Robot.

## Slide 18: 05
Checking that our network is isolated

## Slide 19
In our physical device’s CMD:
Ping “our kali ip” –n 2 Ping our machine’s IP to see if we get a response. ‘-n 2’ means we count two packets to send – you can add any number of packets). We can check our Kali IP in the Kali terminal with the ifconfig command (inet is our address).
We want no response (100 per cent packet loss – this tells us we have no connection)
in our Kali terminal:
Ping 8.8.8.8 –c 2 Ping Google server to see if we get a response. ‘-c 2-’ means we count two packets to send – you can add any number of packets. Note: the command is ‘-n’ in Windows and ‘-c’ in Linux.
Ping “our device’s ip” –c 2 Ping our machine’s IP to see if we get a response. ‘-c 2’ means we count two packets to send – you can add any number of packets. We can check our physical device’s IP in the CMD terminal with the ipconfig command (IPv4 is our address).
We want no response (100 per cent packet loss).

## Slide 20: 06
Our first nmap scan

## Slide 21
sudo stands for either "substitute user do" or "super user do“. It allows you to elevate your current user account to have root privileges temporarily.
nmap is the tool we will use.
-sS is a SynScan, which does not perform a full TCP handshake (does not make a full connection) so is less intrusive.
-T4 will set the scan speed to maximum
10.38.1.110-120 (specifying the range of IP addresses to scan)

## Slide 22
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Leeds City College has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK