## Slide 1: 4.1 Applied mathematical theory in engineering applications
Presenter Name
Time and date
Location
Trigonometry – 4 Answers

## Slide 2
Learning Outcomes
By the end of this session the learner should be able to:
apply trigonometry in various contextualised engineering and manufacturing scenarios.

## Slide 3
240cm
180cm
Starter activity
In a role as an Electrical Engineer, you could be asked to carry out calculations in order to determine the amount of light falling on a given area.
Calculate the amount of light falling on the centre of the table and at the edge of the table.
Answer for the centre of table
800cd
E = I
d2
E = 800
0.1802
E = 246.91 lux

## Slide 4
240cm
180cm
Starter activity
In a role as an Electrical Engineer, you could be asked to carry out calculations in order to determine the amount of light falling on a given area.
Calculate the amount of light falling on the centre of the table and at the edge of the table.
Answer for the edge of table
800cd
E = I x cos ɸ
d2
E = 800 x 0.832
2.162
E = 142.66 lux
180
120
216
= =0.832

## Slide 5
Activity 1
In the role of a mechanical engineer, you could be asked to manufacture a bracket in a workshop environment.
A bracket with bracing halfway along the length is to be made to the specification below. Calculate the amount of material to be used.
1m
1m
+)= 0.707
1m+1m+0.707m
= 2.707m = 2707 mm

## Slide 6
Activity 2
A builder is constructing a roof. However, a structural engineer needs to calculate the length of the beams so that they can be manufactured to the correct specification.
The sloped section of the roof is 6m long, and the peak of the roof needs to be 2.5m high.
What should the angle be between the base of the roof and the slope?
What should the length of the steel beam located across B be?
ɸ
6m
2.5m
B
= = Sin-1 0.42
62 = L2 + 2.52, L= (62 – 2.52) = 5.45
Hence length of beam = 2  5.45 = 10.9
Length of beam to be calculated
L

## Slide 7
Activity 3
In a role as a design engineer, you would need to be aware of the range of the transmissions from a satellite.
A satellite transmitter/receiver is orbiting at an altitude of 2,000 kilometres. If a receiver is located 800km away, how far does the signal travel along length A?
A
2000km
800 km
+) = 2154km

## Slide 8
Example
MJD is a generic engineering company which has decided to expand its range of performance brake discs and are going to offer a brake disc upgrade for the current Mini Cooper S. The diameter of the brake discs is 294mm, and the fixing is a five-hole stud fixing.
The pitch circle diameter (PCD) is 174mm. This is the diameter of the circle passing through the five circles of the stud fixings.
Calculate the spacing from the centre of one hole to
the centre of another hole, “L”.
174mm
L

## Slide 9
Example
360° / 5 (holes) = 72°
180 – 72 = 108°
108/2 = 54°
L/2 = PCD/2 x cos 54
L = 2 x 174/2 x cos 54
L = 102.3
Spacing from the centre of one hole to the centre of another hole = 102.3mm
54°
54°
72°
L
54°
PCD = 174

## Slide 10
Activity 4
MJD is a generic engineering company that manufactures a new Porsche Macan disc upgrade. This is a six-hole stud 360mm fitment.
If the PCD is 240mm, calculate the spacing of the holes.
240mm
360° / 6 (holes) 60°
180 – 60 = 120°
120/2 = 60°
L/2 = PCD/2 x cos 60
L = 2 x 240/2 x cos 60
L = 120mm
Spacing from the centre of one hole to the centre of another hole = 120 mm

## Slide 11
0
Activity 5
In a role as a manufacturing engineer, you have been asked to make a pin for a conduit
bending machine.
Given the information below, calculate the overall length of the component (not drawn to scale).
C
D
C | = | 174mm
D | = | 25mm
0 | = | 50 degrees
=10.49mm
174cm + 10.49m = 184.49mm

## Slide 12
L
L2
Plenary activity
The Venturi duct controls the flow of moisture into a humidifier in a hospital operating theatre. The humidifier’s outlet is 210mm. To concentrate the amount of moisture in the airflow, a reducer needs to be manufactured to reduce it from 500mm to 210mm.
Using the information given in the table to calculate the length of the outlet section of the duct, L2 (not drawn to scale).
L | = | 252cm
L1 | = | 500mm
L3 | = | 450mm
0A | = | 40 degrees
0B | = | 18.9 degrees
0A
0B
210mm
210mm
500mm
145mm
L3 = 450mm
=
L2 = 2 x 29.79 = 59.6mm
L1 = 500mm

## Slide 13
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hertford Regional College has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK